## Slide 1: Wand Case Protype
John Usher
24-Mar-22

## Slide 2: Overview
Design CAD for 3D printing an assembly to house 11 electronic components.
Outer dims of unit is cuboid and approx. 55x210x40 mm.
Comprises:
  1. Lower box (5 sides)
  2. Centre plate.
  3. upper plater.
Electronic boards are mounted using screws.
Box should be approx. 3 mm thick.
Delivery are files suitable for 3D printing the components.

## Slide 3
Button
33 mm O
PLED on its edge
LED of PLED though hole in end plate
ATmega
PLED
PLED
Loudspeaker
Loudspeaker
button
LED
Loudspeaker drivers face down into air gap (5 mm)
I2S audio
30x19
100 x 45 x 21mm
45x17.5
Vent slots below loudspeaker for sound: eg 5 slots, 4 mm width, 30 mm length
IMU
Pi-Zero: 66.0mm x 30.5mm: should be offset to allow access to USB
Pi Zero
40x25
Pi-Zero screws on to case bottom
Micro USB connector at case end
32x25
Same height as OLED
Hole for LED in top plate and middle plate
Screw holes to attach top plate with case
Screw holes
OLED
OLED
27x27
Middle layer of box:
has mounting holes for all
except Pi-Zero
Upper face
Lower face
PLED mounts on to this plate
GPS
GPU antenna
amp
24x15
Hole for antenna wires

## Slide 4
Button
33 mm O
ATmega
PLED
PLED
Loudspeaker
Loudspeaker
button
LED
I2S audio
30x19
45x17.5
IMU
Pi Zero
40x25
32x25
OLED
OLED
GPS
GPU antenna
amp
24x15
WIRING

## Slide 5: Amp
https://www.reichelt.de/de/en/developer-boards-audio-amplifier-class-d-pam8302a-debo-sound-amp1-p235505.html?PROVID=2788&gclid=Cj0KCQjwuMuRBhCJARIsAHXdnqNk4agOJo3q_V-EEzaXOEnxIQZ6iQGCj8q-KR24H9QsqF12Yn-0s_IaApU6EALw_wcB&&r=1
24 x 15 x 2 mm
Class D audio amp

## Slide 6
LARGE Button:
https://www.ozstick.com.au/information/useful-product-info/
Diameter of screw thread = ???
Hole in top plate should ideally have screw thread, if not, then make slightly larger and will just glue in place to hold.

## Slide 7
https://www.amazon.de/-/en/gp/product/B07XJY4VBQ/ref=ppx_yo_dt_b_search_asin_title?ie=UTF8&th=1
SMALL Button:

## Slide 8: Loudspeaker
https://www.berrybase.de/raspberry-pi/raspberry-pi-computer/displays/8-ohm-5w-lautsprecher-passend-f-252-r-waveshare-displays?sPartner=g_shopping&gclid=Cj0KCQiApL2QBhC8ARIsAGMm-KH6kq9ZmpYTb-jLkTrJjl6RPikgvAl0aNnh8y3iC_yK5_bUrXXG-RcaAvE0EALw_wcB&c=56
100 x 45 x 21mm
Note 4 corner screw-holes are half-way in height

## Slide 9: Pi Zero
66.0mm x 30.5mm x 5.0mm
Board should be offset to give access to USB ports

## Slide 10: ATmega328p
https://www.amazon.de/-/en/gp/product/B0755XYBG4/ref=ppx_yo_dt_b_search_asin_image?ie=UTF8&th=1
45 x 17,5 x 18 mm

## Slide 11: OLED
OLED Display I2C 128 x 64 Pixel I2C
https://www.az-delivery.de/en/products/0-96zolldisplay

## Slide 12: GPS
NEO M-9N
https://www.amazon.de/dp/B088LR3488?ref_=pe_3044161_248799201_302_E_DDE_dt_1
NB is board and patch antenna.
Board = 26x36mm
Patch antenna = 25x25 mm

## Slide 13: IMU
https://www.bluedot.space/products/bno055/
30*19*2 mm (NB connector pins are approx 4 mm)
Mounting holes

## Slide 14: PLED (Programmable LED)
Power-Dot 3W, WS2811
https://www.led-genial.de/Power-Dot-3W-WS2811-kompatibel
32 x 25mm
Mounting holes

## Slide 15: I2S Audio
Adafruit I2S Stereo Decoder - UDA1334A
https://www.adafruit.com/product/3678
Product Dimensions: 40.0mm x 25.0mm x 7.1mm

## Slide 16: Micro USB connector
https://www.amazon.de/dp/B07W13X3TD?ref_=pe_27091401_487187591_302_E_DDE_dt_1
10 x 5 x 0.5 cm

## Slide 17: Standard LED